Micro Greenhouse
Vadim Babiy
Daniel Bracamontes
Wesley Nguyen
Jeremy Shaw

---
Upper Level Deck

---
Lower Level Bin

---
Overview
WaterlevelSensor
WaterPumpRelay
Vadim
Jeremy
HeaterRelay
Light
Wesley
FanRelay
FanPWM
Vent Servo
Daniel
HumiditySensor
LightLevelSensor
TemperatureSensor

---
Jeremy
- CLI to directly poll sensors and control peripheral devices
-Web server to give current sensor readouts
-acts as I2C master to drive the I2C bus
Wesley
Daniel

---
Aside: I2C
- Setup in a poll – respond format
- Example:
  - V: bus_write(address, request)
  - J/W/D: onRequest(V, requestedData)
  - V: int x = readNumber()
Jeremy
(11)
Wesley
(12)
Daniel
(13)

---
Jeremy (I2C address 11)
- Sensors abstracted to be presented via i2c
- Relays and light presented to i2c
WaterlevelSensor
WaterPumpRelay
Jeremy
HeaterRelay
Light

---
Wesley (I2C address 12)
Presents Fan control (relay and PWM) to I2C
Wesley
FanRelay
FanPWM
Vent Servo

---
Daniel (I2C address 13)
- Presents Light level reading from ADC to I2C
- Presents Humidity/Temp from DHT11 to I2C
  - DHT11 has a maximum 1Hz refresh cycle, so the interstitial arduino automatically polls the DHT11 and stores the values locally to present to I2C master
Daniel
HumiditySensor
LightLevelSensor
TemperatureSensor

---
Simplification
- Only need one microcontroller with network interface
- Reduce down to two relays:
  - Heater
  - Pump

---
Thanks!